## Slide 1
FARMING FOR WATER EIP
Build a
Small Scale
Wetland Pond
Measure 18 —
Construction & Compliance Guide
Farming for Water EIP Programme
LAWPRO | Teagasc | Dairy Industry Ireland |
Meat Industry Ireland | Dept. Agriculture
farmingforwater.ie

## Slide 2
MEASURE 18 OVERVIEW
Understanding Measure 18
Capture nutrients and sediment before
they reach our waterways.
● Intercepts surface runoff carrying phosphorus and nitrogen
from farmland
● Creates natural habitat for birds, amphibians, insects
and wetland plants
● No planning permission required – no discharge licence needed
● Silt trap at inlet must account for ≥20% of total pond area –
the critical zone for nutrient and sediment removal
Not for: slurry, silage effluent, dairy washings,
or soiled water
Construction guidance: Georgina Mooney, UCD School of Biology & Environmental Science /
Farming for Water EIP (2026)
sizing: 10 m × 6 m × 0.5 m depth
€800
per unit
Standard EIP rate
0.2 ha
maximum pond area
BISS eligibility maintained
1–3
units per holding
Up to €2,400 total
No planning permission
No discharge licence required
farmingforwater.ie

## Slide 3
HOW IT WORKS
The Science of Wetland Ponds
Water Quality Mechanism
Runoff flows into shallow silt trap
(≥20% of pond area, 20-30cm deep)
at inlet
Emergent plants in silt trap slow
velocity and trap sediment-bound
phosphorus
Sediment-bound phosphorus is
trapped and retained
Microbial activity denitrifies nitrogen
at the oxygen-poor base
Emergent plant roots absorb nutrients
from the water column
Clean, filtered water exits via
the raised outlet notch
Counts as a Nature-Based Solution (NbS)
under EU Climate Adaptation Strategy
Biodiversity Co-Benefits
Water Mint — attracts bumblebees & butterflies
Amphibians — frogs and smooth newts colonise within 1–2 years
Insects — dragonflies and damselflies arrive by Year 1
Wetland Birds — snipe, heron, grey wagtail, kingfisher
Invertebrates — support wider farmland biodiversity
Pond creation guidelines: Georgina Mooney, UCD / Farming for Water EIP (2026). A single pond can support dozens of species within its first two seasons.

## Slide 4
SLIDE 04 / SITE SELECTION
MEASURE 18 — CONSTRUCTION GUIDE
Site Selection Criteria
Choose the right location — your pond's performance depends on it.
IDEAL SITES
Impermeable Soils
Heavy clay or gley soils that hold water
naturally without lining
Natural Low Point — topographic depression
where runoff concentrates. Ideally site within
10-20m of an existing wet area or drain —
allows rapid plant colonisation of the new pond.
Along Flow Pathways
In-line with overland flow from intensively
managed fields
Near Drainage Infrastructure
Adjacent to field drains or open channels
Accessible for Maintenance
Machine or foot access without crossing
sensitive ground
Two-Stage Construction — consider partial
installation in Year 1, observe flow paths over
summer/winter, then complete digging in Year 2
for best results.
SITES TO AVOID
Existing Ecological Features
Hedgerows, rush pasture, wet grassland,
or scrub must not be disturbed
Active Floodplains
Will disrupt hydrology and the pond
won't function as designed
Sandy or Free-Draining Soils
Water won't be retained; consider a
willow filter bed instead
Natura 2000 Proximity
SAC, SPA, NHA sites — assess hydrological
connectivity before proceeding
Near Private Wells
Do not site upslope of drinking water
sources or private wells
SOIL
SUITABILITY
Clay / Gley
Proceed — holds water
naturally
EXCELLENT
Loam
May need clay lining
GOOD
Sandy Loam
Lining required or
use alternative
POOR
Peat / Peaty Mineral
Check existing habitat
value first
MODERATE

## Slide 5
POND ZONE SUMMARY TABLE
Zone
Depth
Area
Location
Silt Trap
20–30 cm
≥ 20%
At inlet — must be planted
Mosaic Shelf / Steps
1–50 cm
~ 60%
Throughout — ridges & bumps
Deeper Open Water
50–90 cm
≤ 20%
Throughout — limited
MEASURE 18 — TECHNICAL SPECS
Design and Dimensions
Pond zones per Georgina Mooney / O’Rourke & Loughran (2024)
Source: Georgina Mooney, UCD / Farming for Water EIP (2026)
farmingforwater.ie

## Slide 6
CONSTRUCTION GUIDE
PHASE 1 — STEPS 1 TO 4
Construction Steps: Phase 1
CRITICAL: Do NOT Compact the Basin Flat
A common mistake is compacting the basin entirely flat with the digger.
This prevents plant establishment and reduces biodiversity value.
Leave ridges, hollows and bumps across the basin.
01
Locate
Find the natural low point on
impermeable soil. Confirm
inlet point and outlet direction
before any earthworks begin.
Ideally site within 10–20m of
an existing wet area or drain
to allow rapid plant colonisation.
02
Mark Out
Stake the full perimeter with
canes or spray paint. Allow an
extra 1–2m on each side for
bund material.
03
Strip Topsoil
Remove the top 200mm of
topsoil from the full pond
footprint. Stockpile separately –
keep clean from subsoil.
04
Excavate Basin
Excavate to max 0.5m depth. Form
1:4 slope on inlet side (minimum).
Leave ridges, hollows and bumps
across the basin floor —
do NOT compact flat.
Create mosaic of depths for
plant colonisation.
Tip: Take geotagged photos at each stage –
required for EIP payment claim.
farmingforwater.ie

## Slide 7
MEASURE 18
CONSTRUCTION
STEPS 5 – 8
Construction Steps: Phase 2
Finalise the structure, install the outlet, protect the inlet, and establish the pond margin.
STEP 5
Build the Bund
• Use excavated subsoil –
compact in layers
• Cap with 150mm
stockpiled topsoil
• Target height: 0.3–0.5m
above pond base
On heavy clay – bund may
not be needed
STEP 6
Fit the Outlet Notch
• Set notch 0.1–0.2m above
pond base
• Protects outlet with stone
rip-rap armour
• Options: V-notch weir, pipe
spillway, stone pitching
Ensures permanent water
retention
Protect the Inlet
• Stone apron min 0.5m × 0.5m
at inlet to prevent scour
• Install silt trap at inlet –
min 20% of total pond area,
20–30cm deep
• Plant silt trap with: Bulrush,
Yellow Flag Iris, Water Mint
Silt trap is the most critical
zone for water quality
STEP 7
STEP 8
Fence and Plant
• Stock-proof fence – 2m
buffer from water edge
• Plant silt trap in blocks of
single species (not mixed)
• Do NOT plant Common Reed –
it out-competes all other species
• Rest of pond: allow natural
colonisation if near existing
waterbody
All plants must be locally
sourced and native
Take geotagged photos from multiple angles immediately after construction. Retain contractor invoice – both required for EIP payment claim.

## Slide 8
Zone
Depth
Area
Location
Silt Trap
20–30 cm
≥20%
At inlet — MUST be planted
Mosaic Shelf / Steps
1–50 cm
~60%
Throughout — ridges & bumps
Deeper Open Water
50–90 cm
≤20%
Throughout — limited
FARMING FOR WATER EIP
Pond Construction & Management
Guidelines — Georgina Mooney, UCD (2024)
COMMON MISTAKE TO AVOID
Do NOT compact the basin flat with the digger. A flat, compacted
surface prevents plant establishment and reduces water
quality benefits. Leave ridges, hollows and bumps
throughout the basin.
Semi-permanent island
(submerged winter,
exposed summer)
Outlet
PLANTING
SILT TRAP — Must Plant (in blocks)
Bulrush (Typha latifolia)
Yellow Flag Iris (Iris pseudacorus)
Water Mint (Mentha aquatica)
NO Common Reed — it out-competes
all other species
REST OF POND
Allow natural colonisation if near existing waterbody
Do not remove Horsetails (Equisetum spp.) —
they aid nutrient removal
All plants must be locally sourced and native
Avoid invasive species — may be illegal to plant
POND ZONE SUMMARY
CONSTRUCTION RULES
Silt trap at inlet — min 20% of total pond area
Inlet bank slope — 1:4 gradient minimum
Ridges & hollows along edges and base — essential
Semi-permanent islands encouraged
Natural wavy boundary — not circular
Max inlet-to-outlet distance
Shallow areas (under 20cm) maximised
Pond over 1m deep requires planning permission
MANAGEMENT
MANAGEMENT
VEGETATION
Remove when >70% covered.
Max 30% in one year.
Leave overnight on bank.
Best time: mid-autumn.
DREDGING
3—5 year cycle.
Dredge 1/3 at a time only.
Block outflow with straw bale.
Use sediment as fertiliser off-site.
TREES & SHRUBS
Manage if >70% shading.
3—5 year cycle.
Leave dappled shade.
Keep kingfisher perch branches.
TIMING
Mid-summer preferred — firm
ground, low water.
Avoid disturbing frogspawn (spring)
and hibernating frogs (autumn/winter).
STEP-BY-STEP REFERENCE
10×6×0.5m
Typical size (L×W×D)
€800
Per unit (up to 3)
0.2 ha
Maximum pond area
NO
Planning permission
needed
8 STEPS TO BUILD
LOCATE Natural bowl, basin, impermeable soil, along contour.
Avoid existing watercourses.
MARK OUT Stake perimeter. Confirm in & outlet direction before digging.
STRIP TOPSOIL Remove top 20cm, stockpile separately for pond capping.
EXCAVATE
BUILD BUND
Compact subsoil bank 0.3-0.5m high, cap with stockpiled topsoil.
FIT OUTLET Low point in bund, reinforce with stone. 1-1.5m wide notch.
PROTECT INLET 2.5-5m wide, 1:10 slope at inflow point to prevent erosion.
FENCE & PLANT Set 2m back from water edge. Plant native wetland species.
Max 0.2 ha — larger ponds lose BISS eligibility
Not for slurry, silage effluent or soiled water
Livestock must be excluded — fencing is mandatory
Check proximity to SAC / SPA before construction
No planning permission or discharge licence required
Geotagged photos + proof of costs required for payment
PAYMENT CLAIM:
Geotagged photos + contractor invoice
€800/unit | €627 with ACRES reduced rate | Max 3 units
farmingforwater.ie

## Slide 9
PLANTING GUIDE — TALL EMERGENT SPECIES
Plant Your Pond: Tall Species
Plant silt trap with Bulrush, Yellow Flag Iris and Water Mint — in blocks of single species, not mixed.
Do NOT use Common Reed (Phragmites australis) — it out-competes all other species and will take over the entire pond.
Tip: Horsetails (Equisetum spp.) are highly efficient for nutrient removal — do not remove them if already present on site.
Rest of pond can colonise naturally if near an existing waterbody, ditch or drain.
SILT TRAP
Bulrush
Typha latifolia
0.1–0.5m depth
Dense brown sausage-
shaped spike — very
distinctive
Plant Sept–Nov
SILT TRAP
Yellow Flag Iris
Iris pseudacorus
0–0.3m depth
Bright yellow flowers,
sword-shaped leaves —
late spring
Divide from farm
drain clumps
Branched
Bur-Reed
Sparganium erectum
0–0.3m depth
Branched stem, round
bur-like seed clusters
Plant Sept–Nov
Reed
Sweet Grass
Glyceria maxima
0–0.4m depth
Broad glossy leaves, tall
architectural presence
up to 2m
Plant Sept–Nov
Reed
Canary Grass
Phalaris arundinacea
0–0.3m depth
Upright blue-green
leaves, pale purple-tinged
spikelets
Plant Sept–Nov
Greater
Pond Sedge
Carex riparia
0–0.3m depth
Broad blue-green leaves,
forms large stabilising
stands
Plant Sept–Nov
Source: Farming for Water EIP — Measure 18
farmingforwater.ie

## Slide 10
PLANTING
GUIDE
MARGINAL SPECIES
STEP 4 — ESTABLISH VEGETATION
Planting Guide: Lower Growing Species
Marginal wet zone species — 0 to 0.1m water depth — plant along shallow edges and muddy banks
Fool's Watercress
Apium nodiflorum
● Flowers: July – August
● Depth: Shallow margins, 0–0.1m
● Role: Stabilises pond edges, roots
at nodes
Watercress
Nasturtium officinale
● Flowers: June – September
● Depth: Floating or rooting, 0–0.1m
● Role: Clean water indicator,
native and nutritious
Water Mint
Mentha aquatica
● Flowers: July – September
● Height: Up to 90cm in damp margins
● Role: Pollinator magnet —
bees and butterflies
Brooklime
Veronica beccabunga
● Flowers: May – September
● Height: Low creeping to 30cm
● Role: Stabilises muddy edges,
roots in shallow water
🍃 Source from on-farm drains outside designated SAC / SPA / NHA sites — or use a specialist native Irish wetland plant supplier

## Slide 11
MEASURE 18
Maintenance
LONG-TERM CARE
Maintenance & Monitoring
SCHEDULE
2x
YEAR
Inspect Outlet & Pond
Clear debris, check water levels —
Autumn + Spring
MID-
SUMMER
Bank Vegetation
Firm ground, low water. Best time
for most management tasks.
MID-
AUTUMN
Remove Excess Vegetation
Remove when >70% pond surface covered.
Max 30% removed in one year. Leave cut
material overnight on bank — invertebrates
return to water.
EVERY
3–5 YRS
Sediment De-silting (Silt Trap)
Dredge silt trap on 3–5 yr cycle. Dredge
only 1/3 of pond at a time. Block outflow
with straw bale first. Use dredged
sediment as fertiliser off-site.
EVERY
3–5 YRS
Trees & Shrubs
Manage overhanging vegetation if >70% shade.
Leave dappled light. Keep kingfisher perch
branches. Check bird nesting season.
ONGOING
Deadwood
Add cut branches or a log to pond — benefits
biodiversity, slows water flow, supports
microorganisms.
Avoid disturbing frogspawn (spring) and
hibernating frogs (autumn/winter) when
undertaking management work.
AVOID
No livestock access —
mandatory fencing
always in place
No waste connections —
no slurry, silage effluent,
soiled water
No chemicals in the
fenced buffer zone
Never complete clearance
in one operation
No game fish or
duck stocking
HEALTHY POND ✓
Permanent water year-round
Diverse emergent plant
fringe by Year 2
Frogs and newts
present by Year 2
Dragonflies and damselflies
by Year 1–2
Wetland birds using the margins
(snipe, wagtail, heron)
Clear or lightly turbid water,
no strong odour
farmingforwater.ie

## Slide 12
MEASURME 18
EIP PROGRAMME
Payment & Validation
€800
Per Unit — Standard EIP Rate
Up to 3 units per holding
MAX €2,400
€627
Per Unit — ACRES Rate
When combined with Low Input
Grassland, Extensively Grazed
Pasture, or Intensive Grassland
Next to Watercourse
1-3
Units Per Holding
Each unit max 0.2 ha
BISS Eligible
What You Need to Claim
Geotagged Photos
Minimum 2–3 images,
GPS location embedded
Proof of Costs
Contractor invoice or
materials receipts
EIP Advisor Sign-Off
On-farm verification
required
Compliant Sizing
Pond must not exceed
0.2 ha — fencing in place
Farming for Water EIP — Measure 18
farmingforwater.ie

## Slide 13
COMPLIANCE MEASURE 18
KEY RULES — AT A GLANCE
Compliance Essentials
Maximum Pond Size: 0.2 ha
Larger ponds lose BISS eligibility
No Planning Permission Required
Not classified as a constructed wetland
No Discharge Licence Required
Surface runoff only — no regulated effluent
Livestock Must Be Excluded
Stock-proof fencing is mandatory
Check Natura 2000 Proximity
Assess SAC, SPA and NHA sites before construction
Avoid Existing Ecological Areas
No hedgerows, rush pasture, wet grassland or floodplains
Not for Regulated Wastes
No slurry, silage effluent, soiled water or dairy washings
GAP Regulations Still Apply
S.I. No. 529 of 2020 — nutrient management obligations remain
BISS Eligibility Maintained
While pond area remains under 0.2 ha
Speak to Your EIP Advisor
Required sign-off before and after construction
References
• farmingforwater.ie/measures/small-scale-wetlands-pond/
• Farming for Water EIP Measures Information Booklet (2025), LAWPRO & Teagasc
• S.I. No. 529 of 2020 — EU Good Agricultural Practice Regulations
• Wildflowers of Ireland: wildflowersofireland.net
Talk to Your EIP Advisor Before Construction